## Slide 1
SENSING OF
LOWER LIMB PROSTHESES
Biomedical Robotics
GROUP 9
Ami Sofia Quijano Shimizu – 6193847
Alberto Di Donna – 4944656
Fabio Guelfi – 5004782
Andrea Chiappe - 4673275
Notes: Good morning everyone
We’re group 9 formed by Alberto, Fabio and Andrea, and myself Ami.
And we will address the topic of Sensing of Lower Limb Prostheses.

## Slide 2
TABLE OF
CONTENTS
2
1
3
4
5
6
Why is it important?
Sensing of the lower limb in humans
Modelling of foot sole cutaneous afferents
Invasive Prostheses
Non-Invasive Prostheses
Conclusions
Notes: We will discuss why is it important, how sensing works in humans, a method for modelling the foot sole afferents, how sensing feedback has been implemented in invasive and non invasive prostheses and finally, conclusions on this technology.

## Slide 3
WHY IS IT IMPORTANT?
SENSING OF LOWER LIMB PROSTHESES
Notes: So, first of all, why is sensing feedback an important feature for lower limb prostheses?

## Slide 4
LOWER LIMB
AMPUTATION OF THE
United States: 242, 230
European Union: 87, 088
yearly
amputations
Proprioception
Touch
Sight
Notes: Well, to give you a bit of context, amputation of the lower limb might be more common than we think. There are hundreds of thousands of cases every year globally.
These amputees are often given commercial prosthetic legs which currently do not provide sensory information for the interaction with the environment.
Whats’s the problem with this?
Well, for proper walking and standing, humans rely on the tactile sensing between the soles of the feet and the ground, as well as on proprioception which allows to understand the movement and position of the joints. Because of the lack of this feedback, lower limb amputees wearing classical prostheses become highly dependent on visual feedback and suffer from a variety of functional deficits. Also, these problems increase the rejection or abandonment of prosthetic devices. Therefore, researches have worked on invasive and non-invasive sensory feedback restoration devices that aim at giving sensations of touch and proprioception to the patients for improving their overall performance and confort.

## Slide 5
LOWER LIMB PROSTHESIS
BENEFITS OF SENSING IN
1
Increase of confidence
Increase of walking speed
2
Increase of walking symmetry and balance
4
Reduction of falls
5
3
Reduction of mental and physical fatigue
Notes: Through different types of experiments, as observed in the video, it has been demonstrated that by providing sensory feedback of touch and proprioception, amputees gain significant benefits.
Patients have reported to feel more confidence at wearing a prosthetic leg, even when walking in the dark, up- and down-stairs and on uneven surfaces.
They manage to walk faster
On neuroprostheses, pateints experience a significant reduction of physical fatigue due to the correction of the posture. While in classical prosthesis patients overload their healthy leg which causes back pain, osteoarthritis, and even the risk of heart failure.
There is also a reduction of the mental fatigue or cognitive burden, mainly because they rely less in visual feedback, which allows them to multitask.
4. Symmetric weight distribution helps in increasing walking symmetry, step length, and standing balance
5. This also helps in reducing falls and even anticipating them

## Slide 6
LOWER LIMB PROSTHESIS
BENEFITS OF SENSING IN
1
Increase of confidence
Increase of walking speed
2
Reduction of phantom limb pain
4
Reduction of falls
5
Reduction of phantom limb pain
6
Improved understanding of body-environment interactions
7
3
Reduction of mental and physical fatigue
8
Proprioceptive awareness of prosthesis
Notes: 6. Phantom limb pain is reduced, which is a problem reported to be experienced by 50-80% of amputees
7. Patients experience a better understanding of their environment.
8. and, with proprioception they manage to feel the knee extension and flexion.

## Slide 7
SENSING OF THE LOWER LIMB IN HUMANS
SENSING OF LOWER LIMB PROSTHESES
Notes: Before going at the core of our presentation we do a little step back talking about sensing of the lower limb in humans. This is fundamental, according to us, to have a common language, to understand the problem and to create model

## Slide 8
OF TOUCH
SENSORY NEURONS
Innocuous Stimulation
(LTMRs)
Harmful Stimulation
(HTMRs)
Notes: So now we focus on sensory neurons of touch also called afferents.
They can be divided in 2 class: the one that make us feel innocuous stimulation, called low-threshold mechanoreceptors and the ones that deal with harmful stimulation, called high-threshold mechanoreceptors
low-threshold mechanoreceptors
high-threshold mechanoreceptors

## Slide 9
OF TOUCH
SENSORY NEURONS
Exteroceptive
Proprioceptive
Interoceptive
Innocuous Stimulation
(LTMRs)
Harmful Stimulation
(HTMRs)
Notes: low-threshold mechanoreceptors
high-threshold mechanoreceptors

## Slide 10
IN SKIN
COUTANEOUS MECHANORECEPTORS
LTMRs
SLOW ADAPTING
INTERMEDIATE ADAPTING
RAPIDLY ADAPTING
S.N.
Aβ
Aδ
C
Notes: SN based on size and conduction velocities

## Slide 11
IN SKIN
COUTANEOUS MECHANORECEPTORS
LTMRs
SLOW ADAPTING
INTERMEDIATE ADAPTING
FAST ADAPTING
Notes: The LTMRs are the ones of our interest and they can be divided in slow adapting, intermediate adapting and fast adapting.
The more important are the first ones and the last ones in glaborous skin

## Slide 12
SA I and MERKEL CELLS
Type I: small receptive field, close to surface
Static or low-frequency changes in tissue
Sensitive to stimulus position and velocity
SA II and RUFFINI ENDINGS
Type II: large receptive field, deep in the skin
Skin stretches
Ruffini endings?
Notes: Slow adapting can be divided in 2 type: slow adapting of type 1 associated with mechanosensory ends organs called merkel cells. They are of type 1 because have small receptive fields and are close to the surface. They encode static or low frequency changes in tissue and are hilgly sensitive to stimulus position and velocity
Mechanosensory ends organ

## Slide 13
SA I and MERKEL CELLS
Type I: small receptive field, close to surface
Static or low-frequency changes in tissue
Sensitive to stimulus position and velocity
SA II and RUFFINI ENDINGS
Type II: large receptive field, deep in the skin
Skin stretches
Ruffini endings?
Notes: Slow adapting of type 2 are associated with ruffini endings and are of type 2 because they have larger receptive fields and are deeper in the skin and they encodes skin stretches. The connection with ruffini endings has been only postulate but never demostrated

## Slide 14
FA I and MEISSNER CORPUSCOLES
Type I
Initial and final contact
Poor spatial resolution
The most numerous
FA II and PACINIAN CORPUSCOLES
Type II
High frequency vibration
Notes: Fast adapting of type 1 are associated with meissner corpuscoles and fires at the initial and final contact, have a poorer spatial resolution wrt SA1, but are the most numerous

## Slide 15
FA I and MEISSNER CORPUSCOLES
Type I
Initial and final contact
Poor spatial resolution
The most numerous
FA II and PACINIAN CORPUSCOLES
Type II
High frequency vibration
Notes: Fast adapting of type 2 are associated to pacinian corpuscoles and are extremely sensitive to high frequency vibration

## Slide 16
IN THE CNS
TOUCH CIRCUIT
2 communication methods:
the rate code (firing rate)
the population code (number of fibres activated)
Notes: From skin receptors the signals are sent to the medulla thank to the first order neurons passing through the dorsal column, then a second order neuron transmit the signal to the thalamus and finally a third order neuron take the signal to the somatosensory cortex.
There are 2 type of communication method: the rate code and the population code

## Slide 17
TO NERVES?
HOW TO SPEAK
Notes: We have now seen how cutaneous receptors works and this can help us creating a model of them that can be used to generate biomimetic signals

## Slide 18
MODELLING OF FOOT SOLE CUTANEOUS AFFERENTS
SENSING OF LOWER LIMB PROSTHESES
Notes: So let's focusing on modeling

## Slide 19
MIMICK OF MECHANOTRANSDUCTION PROCESS
FOOTSIM MODEL
Division
in 13 region
Dynamic model
Different density
Same depth for type
firing models
generate spiking output for individual fibers of different afferent classes
Notes: The foot sole is divided in some regions populated with afferents in different density, but the same type are at the same depth. Then there is a dynamic model and finally the firing models that generate spiking output for individual fibers of different afferent classes
mechanical model that computes the deformation of the skin

## Slide 20
IS IT DONE?
HOW
RESULTS...
SOME
Fitting of experimental data
Ramp and hold stimuli
Notes: How has been developed? Thanks to data coming from microneurography where a robot pushes against the foot sole in specific point while with some electrodes we can read the signals in the nerves.
The model fit quite well the experimental data, as we can see in the upper plot and the single afferents fire quite similarly to the real ones descripted before

## Slide 21
IS IT DONE?
WHY
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore
Lorem ipsum dolor sit amet, consectetur adipiscing elit, sed do eiusmod tempor incididunt ut labore et dolore .
Microneurography is not practical in dynamic conditions
We can replicate the activity of afferents while walking
Notes: But why is it done? Microneurography is not practical in dynamic conditions, but with the simulator we can replicate the activity of afferents for example while walking

## Slide 22
USAGE
FOOTSIM
FootSim possible contribution to biomimetic stimulation patterns for tactile feedback restoration in future neuroprosthetics
Notes: So the simulator can be used in order to take in input the pressure and as response generate biomimetic stimulation patterns to be delivered to the central nervous system through the nerves

## Slide 23
INVASIVE PROSTHESES
SENSING OF LOWER LIMB PROSTHESES

## Slide 24
Sensory feedback restoration is fundamental for understanding body-environment interaction or the actual movement of the devices.
Takes information from the sensor on the Neuroprosthesis
Elaborates signals through microcontrollers
Mapping between artificial signals into natural sensory signals
Sends signal back to the brain (through electrodes)

## Slide 25
Transfemoral devices
(above-knee)
Transtibial devices
(below-knee)
Notes: There are two categories of aplutees, transtibial, below knee and transfemoral, above knee. As we can see in teh picture for the transtibial devices the used device sfor restore sensation in the FINE electrodes, coupled with the AMI interface, on nthe other side, on transfemoral prosthesis time electrodes is the most reccomended

## Slide 26
TYPE OF ELECTRODES
Cuff electrodes.
Flat Interface Nerve Electrodes (FINEs).
Longitudinal Intrafascicular Electrodes (wire LIFEs, tf-LIFEs).
Transverse Intrafascicular Multichannel Electrodes (TIMEs).
AROUND
NERVE
THROUGH
NERVE
Notes: LIFE are setted longitudinally througn the nerve
TIME through the nerves via shaft

## Slide 27
FINEs: Reshape the nerve into a flat geometry to increase the interfacing area by moving the axons close to the surface
TIMEs: Penetrate transversally through the nerve for selective access to deeper fascicles.
FINEs: Non-invasive, interact with surface-level fascicles by reshaping the nerve. The metallic contact part with the nerve is called active site.
TIMEs: Invasive, directly target deep fascicles for high-resolution stimulation.
a - A cuff electrode.
b - A C-FINE.
c - A tf-LIFE.
d - A wire LIFE.
e - Cuff electrode biocompatibility in cats.
f - C-FINE biocompatibility in cats
g - tf-LIFE biocompatibility in rats. The arrows point to the electrodes. Scale bar, 100 μm.
h - Wire LIFE biocompatibility in rats. The arrows point to the electrodes. Scale bar, 100 μm
HOW ELECRODES
ARE MADE ?
GEOMETRY AND DESIGN
INTERACTION WITH NERVE TISSUE

## Slide 28
FINEs: Reshape the nerve into a flat geometry to increase the interfacing area by moving the axons close to the surface
TIMEs: Penetrate transversally through the nerve for selective access to deeper fascicles.
FINEs: Made with molded silicone elastomer and stimulating contacts in platinum. ensuring flexibility and surface interaction.
TIMEs: Constructed from micromachined polyimide with Platinum coated with iridium electrodes; require a guiding needle for nerve penetration.
FINEs: Non-invasive, interact with surface-level fascicles by reshaping the nerve. The metallic contact part with the nerve is called active site.
TIMEs: Invasive, directly target deep fascicles for high-resolution stimulation.
a - A cuff electrode.
b - A C-FINE.
c - A tf-LIFE.
d - A wire LIFE.
e - Cuff electrode biocompatibility in cats.
f - C-FINE biocompatibility in cats
g - tf-LIFE biocompatibility in rats. The arrows point to the electrodes. Scale bar, 100 μm.
h - Wire LIFE biocompatibility in rats. The arrows point to the electrodes. Scale bar, 100 μm
HOW ELECRODES
ARE MADE ?
GEOMETRY AND DESIGN
INTERACTION WITH NERVE TISSUE
MATERIALS AND FABRICATION

## Slide 29
FINEs: Reshape the nerve into a flat geometry to increase the interfacing area by moving the axons close to the surface
TIMEs: Penetrate transversally through the nerve for selective access to deeper fascicles.
FINEs: Made with molded silicone elastomer and stimulating contacts in platinum. ensuring flexibility and surface interaction.
TIMEs: Constructed from micromachined polyimide with Platinum coated with iridium electrodes; require a guiding needle for nerve penetration.
FINEs: Non-invasive, interact with surface-level fascicles by reshaping the nerve. The metallic contact part with the nerve is called active site.
TIMEs: Invasive, directly target deep fascicles for high-resolution stimulation.
a - A cuff electrode.
b - A C-FINE.
c - A tf-LIFE.
d - A wire LIFE.
e - Cuff electrode biocompatibility in cats.
f - C-FINE biocompatibility in cats
g - tf-LIFE biocompatibility in rats. The arrows point to the electrodes. Scale bar, 100 μm.
h - Wire LIFE biocompatibility in rats. The arrows point to the electrodes. Scale bar, 100 μm
HOW ELECRODES
ARE MADE ?
GEOMETRY AND DESIGN
INTERACTION WITH NERVE TISSUE
MATERIALS AND FABRICATION

## Slide 30: SENSORY FEEDBACK RESTORATION LOWER-LIMB EXTREMITIES
FINEs tested for transtibial amputee
TIMEs tested for transfemoral amputee
FINEs: evoke sensations on spatially extended areas (important for balance and locomotion).
TIMEs: evoke spatially selective sensations (touch, pressure, vibration)
The neural feedback was then exploited in motion task
Led to greater prosthesis embodiment, more confidence and reduced cognitive effort during prosthetic use.
RESTORING SENSATIONS VIA SCIATIC NERVE STIMULATION
FUNCTIONAL IMPROVEMENT

## Slide 31
A surgical approach connecting agonist and antagonist muscle-tendon pairs.
Restore proprioceptive sensations (transtibial amputee)
This technique give back information about speed and force, which is then perceived as physiological joint proprioception
Multiple AMI pairs can enable control and sensation for various prosthetic joints.
SENSORY FEEDBACK RESTORATION LOWER-LIMB EXTREMITIES
AGONIST–ANTAGONIST MYONEURAL INTERFACE
(AMI)

## Slide 32: ELECTRODES OPTIMIZATION
Developing an anatomically sciatic nerve model
Finite Element Model (FEM) for electric potential calculation
Electro-neuro model (ENM) to simulate invasive neural stimulation.
HYBRID FEM-NEURON MODEL
The FEM-NEURO MODEL is used for testing and evaluate the efficiency of TIMEs and FINEs electrodes with different active site configurations.
The goal was to find the optimal interface to use in human subjects, their surgical placement and beneficial policy of stimulation
METHODS
TIMEs and FINEs electrodes with 20 active site are optimal for lower limb.
To interface the huge sciatic nerve, model indicates 3 TIMEs is the optimal number of surgically implanted electrodes
RESULTS

## Slide 33
NON-INVASIVE PROSTHESES
SENSING OF LOWER LIMB PROSTHESES

## Slide 34
CLASSIC
NON-INVASIVE
No sensing information
No knee joint position awareness
Acoustic or visual sensing
Motorization system
Discrete information

## Slide 35
NEUROLEGS
NON-INVASIVE
Electro-cutaneous stimulation in real-time
Non-invasive approach
Sensorized footsole & knee angle perception
Tactile and proprioceptive feedback
Skin electrodes at the thigh level
Graphical user interface for patient and trainer
Compliant with standard regulations
Fully portable device & easy to wear

## Slide 36
TACTILE FEEDBACK
FOOT SOLE
Three electrodes to give the modular stimulation of the foot regions:
Toe
Middle part
Heel
Every electrode has at least 5 cm distance to not overlap the stimulation
The microcontroller computes and remaps the information for the electrodes
Seven forces sensors in the foot sole

## Slide 37
ELECTRO FEEDBACK
KNEE ANGLE
Two IMU sensors (green boxes) to perceive the rotation angle of the knee
One electrode on the hip to provide the stimulation
Fundamental for symmetry and balance, to reduce the risk of falling
Microcontroller with the encoder to remap with linear relation the signal

## Slide 38
STIMULATION
CONFIGURATION
The sensors send the feedback information to the controller through BLTE technology.
All this at real time to improve the quality of life
~ latency of less than 50ms for all pulsewidths computation
Long life cycle battery
The system controller sends all the information to the cloud to see them on the user and trainer app
Controller, with C++ algorithm encodes the information and transforms them into a signal in the electric space with 80Hz of frequency, modulated pulsewidth and calibrated amplitude

## Slide 39
CALIBRATION
Knee calibration: Two IMU calibrations to estimate the angle of the knee
EMBEDDED
Pulsewidth calibration: Walk maximum force exerted related to maximum pulsewidth

## Slide 40
CALIBRATION
Sensation characterization requires the clinician, for the very first time
GRAPHICAL INTERFACE
Different stimulus to find the optimal electrical parameters
User can increase or decrease the amplitude
Emergency button for safety reason

## Slide 41
CALIBRATION
User can increase or decrease the amplitude constant value of the pulses of the 10%
USER GUI
The user has the possibility to press Emergency button on the app to perform a safety stop of the system

## Slide 42
TESTS & COMPETITIONS
SYSTEM VERIFICATION
Test
Each single components
3 healthy patient to test the system
3 amputees tested the product and all of them increase in gait symmetry (much less swing), confidence and steps balance
CYBATHLON They participates in three competitions getting always good placement also against much more expensive and complex prosthesis

## Slide 43
CONCLUSION
LOWER LIMB SENSING

## Slide 44
NON INVASIVE
VS
TYPE | PROS | CONS
INVASIVE | Higher sensitivity Higher precision Better embodiment Reduced cognitive load Highly intuitive | Surgical risks Very expensive Complex maintenance Irreversible Longer approval processes
NON-INVASIVE | Security and ease of use Lower cost Higher adaptability Not limited to non-amputees | Less accuracy Sensory feedback limitation Environmental Interferences Frequent calibration required Lot of training required
INVASIVE
Notes: Invasive and non invasive solutions have pros and cons. The invasive one excels in higher sensitivity, precision, embodiment and intuition since the signals are directly sent to the nerves. However, it comes at higher costs, surgical risks, and complex maintenance.
On the other hand, non invasive devices excel in their low cost, adaptability, and security; while they have limitations on accuracy, level of sensory feedback, interferences and constant training and calibration.

## Slide 45
CHALLENGES
CURRENT
1
Improving materials to reduce long-term degradation/wear/failure of devices, both internal and external
2
Economical accessibility
3
Achieving natural and intuitive sensations.
GOALS
LONG-TERM
1
Extending the system to a 2-leg system to enlarge target population
2
Test system on more diversified scenarios for expanding usability
3
Test system also for rehabilitation for restoring neural pathways and reducing phantom pain
Notes: Current challenges of this technology include the improvement and development of materials resistant at long term use and with medical grade use,
Economical accessibility
And achieving natural sensations, since it is still one complaint from the users.
This technology has a lot of potential for the future including extending the device to a 2-leg system,
Do tests in more diversified scenarios
And validating its use for rehabilitation for restoring neural pathways and reducing phantom limb pain.

## Slide 46
LIST OF
REFERENCES
Katic N, Siqueira RK, Cleland L, Strzalkowski N, Bent L, Raspopovic S, Saal H. Modeling foot sole cutaneous afferents: FootSim. iScience. 2022 Dec 24;26(1):105874. doi: 10.1016/j.isci.2022.105874. PMID: 36636355; PMCID: PMC9829801.
Raspopovic S, Valle G, Petrini FM. Sensory feedback for limb prostheses in amputees. Nat Mater. 2021 Jul;20(7):925-939. doi: 10.1038/s41563-021-00966-9. Epub 2021 Apr 15. PMID: 33859381.
Abraira VE, Ginty DD. The sensory neurons of touch. Neuron. 2013 Aug 21;79(4):618-39. doi: 10.1016/j.neuron.2013.07.051. PMID: 23972592; PMCID: PMC3811145.
Basla C, Chee L, Valle G, Raspopovic S. A non-invasive wearable sensory leg neuroprosthesis: mechanical, electrical and functional validation. J Neural Eng. 2022 Jan 24;19(1). doi: 10.1088/1741-2552/ac43f8. PMID: 34915454.
Petrini, F.M., Bumbasirevic, M., Valle, G. et al. Sensory feedback restoration in leg amputees improves walking speed, metabolic cost and phantom pain. Nat Med 25, 1356–1363 (2019). https://doi.org/10.1038/s41591-019-0567-3
Video lesson. Professor S. Raspopovic at 8th Summer School of Neuroengineering, Genova, 2022

## Slide 47
THANK YOU
ANY QUESTIONS?